## Slide 1: Recursive x86-64 Assembly Program for Calculating Factorial
Lars Lundberg
(see also youtube video on: https://www.youtube.com/watch?v=J_QMs3ImO_8)

## Slide 2: Overview
We will look at an x86-64 assembly version corresponding to a recursive C-program
We will see how the Stack is used in an assembler program
The Stack works like a LIFO (Last In First Out) storage.
  Push register – store a register on the Stack
  Pop register – remove data from the Stack and put that data in the register
  The stack is also used to store the return address after a function call

## Slide 3
Push
Pop
Stack
Push
Push
Push
Pop
Pop
Pop

## Slide 4
Push
Pop
Stack
Push
Push
Push
Pop
Pop
Pop

## Slide 5: Recursive C function for factorial
long rfact(long n)
{
long result;
if (n <= 1)
result = 1;
else
result = n*rfact(n-1);
return result;
}

## Slide 6
C code
long rfact(long n)
// n stored in rdi
{
long result;
if (n <= 1)
result = 1;
else
result = n*rfact(n-1);
return result;
}
//result returned in rax
X86-64 assembly code
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq

## Slide 7: An Example
int main()
{
…
long fact4 = rfact(4)
…
}
…
movq $4, %rdi
call rfact
.L36: movq %rax, fact4
…
We assume that the address of .L36 is 2000, and that the address of the imul-instruction just before .L35 is 1000 and that the stack pointer (%rsp) is 3000. We also assume that %rbx is 555. We use decimal numbers

## Slide 8
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 555 2992:
rsp: 2992
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 9
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 555 2992: 555
rsp: 2984 2984:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 10
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 11
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984:
rax: 1
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 12
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984:
rax: 1
ZF: 0 …
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 13
Registers Mem adr Stack
rdi: 4 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984:
rax: 1
ZF: 0 …
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 14
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984:
rax: 1
ZF: 0 …
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 15
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 4 2992: 555
rsp: 2976 2984: 1000
rax: 1 2976:
ZF: 0 …
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 16
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 4 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 17
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 18
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 19
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 20
Registers Mem adr Stack
rdi: 3 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 21
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 22
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 3 2992: 555
rsp: 2960 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 23
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 3 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 24
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 25
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 26
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 27
Registers Mem adr Stack
rdi: 2 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 28
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 29
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2944 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952: 1000
2944:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 30
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2936 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 31
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 1 2992: 555
rsp: 2936 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 32
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 1 2992: 555
rsp: 2936 2984: 1000
rax: 1 2976: 4
ZF: 0 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 33
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 1 2992: 555
rsp: 2936 2984: 1000
rax: 1 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 34
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 1 2992: 555
rsp: 2936 2984: 1000
rax: 1 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 35
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2944 2984: 1000
rax: 1 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the fourth time

## Slide 36
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 1 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 37
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 2 2992: 555
rsp: 2952 2984: 1000
rax: 2 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 38
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 3 2992: 555
rsp: 2960 2984: 1000
rax: 2 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the third time

## Slide 39
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 2 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 40
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 3 2992: 555
rsp: 2968 2984: 1000
rax: 6 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 41
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 4 2992: 555
rsp: 2976 2984: 1000
rax: 6 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the second time

## Slide 42
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984: 1000
rax: 6 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 43
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 4 2992: 555
rsp: 2984 2984: 1000
rax: 24 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 44
Registers Mem adr Stack
rdi: 1 3000: 2000
rbx: 555 2992: 555
rsp: 2992 2984: 1000
rax: 24 2976: 4
ZF: 1 … 2968: 1000
2960: 3
2952: 1000
2944: 2
2936:
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq
We enter rfact the first time

## Slide 45: Back again
int main()
{
…
long fact4 = rfact(4)
…
}
…
movq $4, %rdi
call rfact
.L36: movq %rax, fact4
…
rdi: 1
rbx: 555
rsp: 3000
rax: 24 (will be stored in fact4)

## Slide 46
C code
long rfact(long n)
// n stored in rdi
{
long result;
if (n <= 1)
result = 1;
else
result = n*rfact(n-1);
return result;
}
//result returned in rax
X86-64 assembly code
rfact: pushq %rbx
movq %rdi, %rbx
movq $1, %rax
compq $1, %rdi
jle .L35
decq %rdi
call rfact
imulq %rbx, %rax
.L35: popq %rbx
retq